## Slide 1: Implementation of Semi-Autonomous and Fully-Autonomous Parking Features for the DE2Bot
Yotam Ghebre
Kevin Hilinski
Sebastian Jara Garay
Brian Mull
Joey Sterling
ECE 2031 Digital Design Laboratory L01
Georgia Institute of Technology
April 18, 2017
Notes: Introductions

## Slide 2: Project Objectives
Implement a semi-autonomous perpendicular parking function in the DE2Bot
Implement a semi-autonomous parallel parking function in the DE2Bot
Implement a fully-autonomous perpendicular parking function in the DE2Bot
Parking lot image source: Assignment Sheet: Design Proposal
Notes: Yotam

## Slide 3: Design Solution
Robot is in manual mode unless “0” is pressed
Robot returns to manual mode once autonomous parking is completed
All autonomous operations are composed up of 4 basic movements
Notes: Yotam

## Slide 4: Manual Driving Operation
Remote image source: Infrared TV Remote Manual
Notes: Kevin

## Slide 5: Semi-Autonomous Perpendicular Parking Operation
Manually drive to desired position
Press “7” to execute automatic-parking maneuver
Parking lot image source: Assignment Sheet: Design Proposal
Notes: Kevin

## Slide 6: Semi-Autonomous Perpendicular Parking Execution
Reset position for greater accuracy
Check for vacancy of the spot
  Use sonar for detection
Drive 47.4 cm into parking spot

## Slide 7: Semi-Autonomous Parallel Parking Operation
Manually drive to desired position
Press “9” to execute automatic-parking maneuver
Parking lot image source: Assignment Sheet: Design Proposal
Notes: Kevin

## Slide 8: Semi-Autonomous Parallel Parking Execution
Reset position for greater accuracy
Check for vacancy of the spot
  Use sonar for detection
Drive 32.9 cm into parking spot

## Slide 9: Fully-Autonomous Perpendicular Parking Initiation
From the starting space outside of the parking lot, “0” is pressed on the remote to enter fully-autonomous mode
To select a destination parking spot, button “1” through “7” will be pressed corresponding to the parking spot number
Notes: Joey

## Slide 10: Fully-Autonomous Perpendicular Parking Maneuver
Once a spot is selected, the following sequence of movement instructions will follow:
Notes: Joey

## Slide 11: Fully-Autonomous Maneuver Diagram
(0,0)
(51.2 cm,0)
(51.2 cm, -97.5 cm)
+x
+y
Parking lot image source: Assignment Sheet: Design Proposal
Notes: Joey

## Slide 12: Problems Encountered
Drifting caused by using DVel to control wheel speed
Increased speed reduced stopping accuracy
Slack in wheels was causing error in odometer readings
Parking lot image source: Assignment Sheet: Design Proposal

## Slide 13: Improving Drift
Calling the provided control movement function in an endless loop results in more accurate robot movement
  As opposed to an external interrupt updating the speed of the robot every 0.1 seconds
Decreased speed (slow speed) in order to reduce overall drift
Notes: sebastian

## Slide 14: Improving Parking Execution
Created special autonomous parking distances
  Spot 5,6,7 = 50.96cm
  Spot 1 = 44.30cm
Readjust wheel slack by rolling bot into starting block
Left Wheel
Right Wheel
Wheel image source: www.openclipart.org
Notes: motors engage at different times

## Slide 15: Results of Pre-Demo Fully-Autonomous Trials

## Slide 16: Results of Pre-Demo Semi-Autonomous Trials

## Slide 17: Demo Results

## Slide 18: Special Features
Autonomous Pause and Abort
  “5” pauses
  “5” again aborts autonomous and resumes manual control
  “0” resumes autonomous parking
5° adjustment
  for semi-autonomous parking
  “1” shifts left
  “3” shifts right
Notes: Kevin

## Slide 19: Future Work
Sonar
  safety stop in semi-autonomous parking
  drift correction in autonomous parking
  start correction
Speed
  improving speed control to allow for faster parking
DE2Bot image source: DE2Bot User’s Manual
Notes: Brian

## Slide 20: Conclusions
Strengths
  Intuitive and user friendly control layout
  Improved Accuracy
  Automatic parking pause and abort
Simple control instructions for future implementations
Notes: Brianz

## Slide 21: Questions?